## Slide 1
SEES Facility Overview
and
Tomography and Rock Mechanics at SEES
Mark Rivers
GeoSoilEnviroCARS
Center for Advanced Radiation Sources
University of Chicago

## Slide 2
1
2
3
4
5
6
7
8
11
10
SEES at APS: Sectors 3, 6, and 13 (~20 FTE)
X-rays
12
11
X-ray microprobe (XRM)
Surface/interface scattering
Computed micro-tomography (CMT)
Nuclear resonance scattering (NRS)
Diamond anvil cell
high pressure (DAC)
Large volume press
high pressure (LVP)
X-ray absorption
spectroscopy (XAS)
Offline user laboratories

## Slide 3
6
10
SEES at NSLS-II (3 FTE)
12
XPD (28-ID-2): High P,T
Mineral Physics
FIS (22-IR-1): High P Infrared spectroscopy
XFM (4-BM): X-ray Fluorescence Microscopy

## Slide 4
10
SEES at ALS (5 FTE)
12.2.2: High P,T
Mineral Physics
8.3.2: Tomography
In Situ Rock Deformation
Haboub et al. 2014
5.3.2, 7.0.1.2, 11.0.2.2: SYSTER
SYnergy of Soft and Tender X-rays for Earth Research
0.1 µm
Organic
Inorganic

## Slide 5
10
SEES at SSRL (1 FTE)
Imaging beamlines: 2-3, 6-2b, 7-2, 14-3b
XAS beamlines: 4-1, 4-3, 7-3, 9-3, 11-2, 14-3a

## Slide 6
10
APS-U High-Brightness Storage Ring Lattice
eo = 3100 pm.rad
eo = 42 pm.rad
Upgraded APS, 7-bend lattice
Original APS, double-bend lattice
Original APS
Electron beam profile in undulator straight section
Magnetic lattice in one sector
Increasing the number of bending magnets results in much lower emittance and much higher X-ray brightness
APS Upgrade

## Slide 7
10
APS-U Beamline Upgrades
New and updated insertion devices for optimum spectral performance.
9 new feature beamlines + Long Beamline Building (green)
14 enhanced and improved beamlines
SEES beamlines 3-ID and 13-ID received funding for upgrades from APS-U project
NSF-SEES funding provided additional upgrades for all SEES beamlines
18 bending magnet beamline relocations

## Slide 8
10
The APS Upgrade
Project cost: $815M
Machine shut down: April 17, 2023
First beam in new machine: April 10, 2024
Beamlines started commissioning: June 17, 2024
July 20, 2023
June 29, 2023
Final module installation
December 2023

## Slide 9
10
The APS Upgrade
APS is now the brightest synchrotron in the world!
Current in 324 bunch mode: 200 mA (twice the old APS)
Current in 48 bunch mode: 140 mA (implementing plan to reach 200 mA)
Number of beamlines returned to General User Operation: 26
Number of beamlines in Technical and Scientific Commissioning: 30
All SEES APS beamlines back in General User Operation for 2025-3 except 13-ID-C/D which is commissioning a new DAC table, focusing optics, and rebuilt diffractometer.
Still installing new X-ray optics and instrumentation
13-ID-D DAC system
13-ID-C Diffractometer
3-ID-C
laser heating system

## Slide 10
1
2
3
4
5
6
7
8
11
10
SEES Tomography Facility at APS Beamline 13-BM-D
X-rays
12
10
11
User facility with a broad range of geoscience applications (soils, fossils, meteorites, etc.)
Bending magnet source, critical energy 15.6 keV
Beamline modes, unique to this beamline:
  Monochromatic beam, 10-80 keV, Si (111)
  Pink beam, 1.1 m long vertical mirror
    Can be bent to focus or defocus
    High energy cutoff 15-100 keV
  White beam with low-energy cutoff filters
Both ambient/low-pressure and very high-pressure tomography
Tomography runs about 30% of the time
  Several non-tomography techniques share this station

## Slide 11
1
2
3
4
5
6
7
8
11
10
SEES Tomography Facility at APS Beamline 13-BM-D
X-rays
12
10
11
Sample stage:
  Aerotech air-bearing rotation stage with slip-ring to X-Y stage for continuous rotation
  Mounted on Aerotech hexapod for X-Y-Z translation and 3 rotations
  25 kg load capacity
Optics:
  Nikon macro lens and Mitutoyo 5X and 10X objectives for 1.4-15 mm field of view
Cameras:
  FLIR Grasshopper (1920x1200 pixels) and Oryx (2448x2048), each up to 163 frames/s.
  Mikrotron CoaXPress camera (1920x1080) up to 2,247 frames/s.

## Slide 12: In-Situ Cells used at 13-BM-D Heitt Mjolnir Cell (Freitas et al., 2023)
30 MPa confining pressure
600 MPa axial load
10 mm sample diameter, 20 mm length
Sample temperature to 300°C
Continuous fluid flow through sample
Aluminum sample chamber for good X-ray transmission.
Commissioned with Wenlu Zhu’s group in May and July 2025
New carbon-fiber and glass-fiber sample chambers for better X-ray transmission at lower confining and axial pressure.
Confining pressure
Pore pressure
Lower heater
Lower thermocouple
Load cell
LVDT
Axial fluid

## Slide 13: In-Situ Cells used at 13-BM-D
Mjolnir tri-axial cell
After Butler et al. 2020.
3mm diameter, 10 mm long
50 MPa confining pressure, 600 MPa axial load
Modified Mjolnir
For granular media studies
PEEK sample chamber, 11mm chamber ID.
Stepper motor axial load

## Slide 14: In-Situ Cells used at 13-BM-D
Mjolnir-like cell
From Parisa Shokouhi’s group at Penn State
Ultrasonic velocity and acoustic emission capabilities
Pumping cart
Used for Mjolnir and other cells
2 ISCO 65D pumps for confining and axial load
Vindum VP-12K dual pump for continuous fluid flow
GE Druck PACE-5000 for gas pressure to 15 MPa

## Slide 15: In-Situ Cells used at 13-BM-D
Tri-axial cell
From Giuseppe Buscarnera’s group at Northwestern University
Used for oedometric studies (rigid walls) of granular media
Tri-axial cell
From Giuseppe Buscarnera’s group at Northwestern University
Flexible membrane containment.
Sample loaded under vacuum.
Used for studies of granular media like sands.

## Slide 16: In-Situ Cells used at 13-BM-D
Cryogenic cell
Used for studies of thermal deformation granular media from -120°C to +20°C
Cold nitrogen gas from an Oxford CryoJet flows down the metal tube into the sample chamber.
High-temperature cell
Used for studies of thermal deformation granular media up to 140°C.
Gas flows through ceramic tube with heating element.

## Slide 17: X-ray Radiography and Ultrasonic Velocity Studies of Rock Fractures in a Triaxial Cell Parisa Shokouhi and Jacques Riviere (Penn State U.)

## Slide 18: Tomography for Reaction-Driven Melt Channeling Megan Ryan and Wenlu Zhu (Univ. of Maryland)
Reaction-driven melt channel in rock with initially 20 vol % melt
Reaction-driven melt channel in rock with initially 4 vol % melt
Melt channel
Reaction layer
Melt channel
Reaction layer
3-D X-ray microtomography of melt channels is used to identify fine details of melt microstructures. Once segmented, digital permeability experiments can be used to quantify the permeability of reactive melt channels.
For more information, see Ryan et al., Poster #29
Melt source – partially molten rock – sink triplets after experiment (Pec et al., 2017)
Previous CT scans were unable to resolve fine details of 3-D melt microstructures.
Experimental

## Slide 19: Capturing Reaction-Induced Fracturing due to Carbonation Reaction in Rocks Tommaso Mandolini, Travis Hager, and Wenlu Zhu (Univ. of Maryland)
Carbonation: clogging vs cracking in ultramafic rocks
Carbonation facilitating cracking: interplay between the “mudcracks” on the surface and the dissolution etch-pits inside an ultramafic rock.
Zhu et al., 2016
Xing et al., 2018
In-situ, synchrotron-based X-ray tomography showing evolution of reaction-induced fracturing due to carbonation in periclase (MgO)
Magnesite
Example of Magnesite precipitation along crack walls (modified after Lisabeth et al., 2017)
MgO + 2NaHCO3
MgCO3 + Na2CO3 + H2O
MgO + H2O
Mg(OH)2
Magnesite
Brucite
2 µm
∼2.5 mm

## Slide 20: High-P tomography: 3D imaging at P-T
Die set
Harmonic
Drive
Transport
Rails
250 T press frame
Hydraulic
ram
Reconstruction
33% SiO2
(v-forsterite)
803 µm
Radiographs
(180º @ 0.5º)
Wang et al., RSI, 2005
APS 13-BM-D
Measure density of amorphous materials by directly measuring volume

## Slide 21: Simulate Volcanic Degassing under High Pressure Tomography and Acoustic Emission in a Paris-Edinburgh cell
Phase diagram of carbonated, fertile peridotite
Falloon & Green, EPSL, 1989
T. Hammouda, T. Officer, T. Yu, M. Yakovlev, Y. Wang (Blaise Pascal Univ. and U Chicago) in prep.
Cell assembly
PE anvil
AE transducer
Decompression-induced degassing and melting produce acoustic emissions (micro-eruptions), which are located within and around the sample.
In-situ tomo shows bubble formation during decompression at high T
Approx. locations of AE events

## Slide 22: Correction of Motion Artifacts in High-Pressure Tomography
Max Yakovlev, University of Chicago
High-pressure tomography frequently has motion artifacts:
Sample vertical motion during scan due to compaction of the media or sample
Sample horizontal wobble during scan due to imperfection in high-load thrust bearings
Max has developed software to correct these artifacts, resulting in dramatically improved reconstructions
For more information, see Yakovlev et al., Poster #38

## Slide 23: Tomography at ALS Beamline 8.3.2
In-Situ Environments
Low temperature triaxial cell:
  Up to 80 C, 24 MPa confining pressure, 40 MPa axial stress, 2-phase fluid injection
High temperature triaxial cell:
  Up to 400 C, 24 MPa confining pressure, 40 MPa axial stress
Cryo/lunar cell:
  Down to -180C, high vacuum, in-situ ultrasonic measurement
Hot stage:
  Up to 2000 C with parabolic lamps, compression and tension
Cryo/lunar cell
Low-T triaxial cell
Superconducting bending magnet source
SEES is providing post-doctoral scientist through UC Santa Cruz (offer accepted, awaiting visa)
Collaboration with ALS and LBNL BES Geosciences Division
Also have nano-CT capabilities on beamline 11.3.1, not in general-user program
ALS will shut down for ALS-U, perhaps starting in summer 2026 with expected 2-year dark time

## Slide 24: Future Plans – APS 6-BM-B Station
Plan to add tomography capabilities at SEES APS 6-BM-B station
Instrumentation for both lower-pressure (brittle) and higher-pressure (ductile) regimes
Up to 100 kg load capacity for larger in-situ cells like Paris-Edinburgh.
Major components:
  New press base for SAM-85 press and tomography experiments combined with energy-dispersive diffraction (Received, installation soon)
  Upstream table optimized for tomography and brittle deformation. Hexapod base, optimized imaging system. (Design phase)
  Air bearing rotation stage with ~100 kg load capacity (Received)
  Pumping system with 4 syringe pumps for confining pressure, axial load, and continuous fluid flow. (Components received)
  X-ray vertical deflecting mirror to provide focused beam for diffraction and defocused beam for tomography. (Design phase)

## Slide 25: Possible Future Plans – NSLS-II HEX Station
Characteristics
  Superconducting wiggler, 29 poles, 4.3 Tesla
  Double bent Laue monochromator with large bandwidth
  100 mm x 20 mm beam in station 100 m from source
  Mono or white beam modes
Group from UChicago, U Maryland, and Stony Brook ran at HEX in 2023 and 2024 to test it for triaxial cell experiments
  Tomography with monochromatic beam at 40 and 60 keV
  White beam tomography, adjusting wiggler field for optimum contrast
  Energy-dispersive diffraction with the strip detector
Conclusions
  HEX is a unique beamline in the U.S. with high energy, large beam, high flux.
  The SEES NSLS-II Partner User Proposal now includes HEX, but with no guaranteed time.
  It is a station we should consider carefully for future SEES plans.
Granite after failure in triaxial cell
Wenlu Zhu mounting Mjolnir cell

## Slide 26
1
2
3
4
5
6
7
8
11
10
Getting Beam Time
X-rays
12
10
11
All SEES beamtime is awarded through the facility-specific general user proposal systems, with a preference for earth and environmental science research.
Potential tomography users should contact the beamline scientists to discuss feasibility and beamtime requirements.
We will work with you to accommodate and help design sample cells.
Thanks for your attention!!!