## Slide 1
Multiscale observations of deformation in porous rocks based on full field measurements
Université Grenoble Alpes, CNRS, Laboratoire 3SR
Grenoble, France
Pierre Bésuelle
4th ISRD-RCN workshop – 21-23 May 2024 – Grenoble, France

## Slide 2
Introduction
1
Strain localisation is a major failure process in porous rocks, well-known to be mean-stress dependant.
  However, experimental characterisation is mainly limited to axisymmetric conditions (axisymmetric compression tests, axisymmetric extension tests)
  Not representative of real in situ stress states, quite particular in term of localisation conditions
  Only a few experimental devices for elementary tests in rock mechanics are not axisymmetric: plane strain compression, true-triaxial cell, …
in operando full field measurements allow to detect and characterise strain localisation
Extended experimental characterisations with
  a true-triaxial cell using in operando 2D full field kinematic measurement
  axisymmetric cell using in operando 3D full field kinematic measurement
Mesoscale deformation mechanisms characterisation is needed to understand deformation: constitutive modelling, multiscale modelling.
  post mortem analysis
  in operando hight resolution full field measurements
Constitutive behaviour of rocks, mechanisms of deformation, strain localisation

## Slide 3
Introduction
1
Constitutive behaviour of rocks, mechanisms of deformation, strain localisation
Bésuelle P., Desrues J. and Raynaud. S., 2000, Experimental characterisation of the localisation phenomenon inside a Vosges sandstone in a triaxial cell. Int. J. Rock Mech. Mining Sci., Vol. 37, n° 8, pp. 1223-1237.
Bésuelle P., Baud P. and Wong T.-f., 2003, Failure mode and spatial distribution of damage in Rothbach sandstone in the brittle-ductile transition. Pure Appl. Geoph., Vol. 160, n° 5-6, pp. 851-868
3 = 20 MPa
3 = 50 MPa
How the emergence of digital images analysis contributes to improve experimental characterisation in rock mechanics ?
x-ray CT on sandstone specimens after loading
Experimental characterisation on a sandstone
SEM post mortem
Notes: a quick review of what we were doing 20-25 years ago, to consider developments since then.

## Slide 4
Outline
Introduction
Materials
  Red Vosges sandstone
  Callovo-Oxfordian clay rock
Experimental loading devices and in situ full field measurements
  True triaxial cell with 2D-imaging
  Triaxial cells for lab and synchrotron x-ray CT
Strain localisation and small scale deformation in sandstone
  Strain localisation macro-scale characterisation (2D-DIC)
  2D post mortem meso-scale analysis (SEM)
  3D in situ meso-scale analysis (lab x-ray CT)
Strain localisation and small scale deformation in a clay rock
  Strain localisation macro-scale characterisation (2D-DIC)
  2D post mortem micro-scale analysis (BIB-SEM)
  3D in situ meso-scale analysis (ESRF ID19 x-ray CT + 3D-DIC)
Conclusions

## Slide 5
Materials
Red Vosges sandstones (eastern France):
‘Isotropic’ Woustwiller sandstone
  Porosity 21 %
  Mean grain size d50 ~ 300 µm
  95% quartz, 5% microcline, 1% mica, 1% kaolonite
Anisotropic Hangviller sandstone
  Porosity 22.6 %
  Mean grain size d50 ~ 300 µm
  88% quartz, 8% microcline, 3% mica, 1% kaolinite
  Natural bedding with alternating bi-modal porosity
    1-2 mm thick low porosity layer
    2-4 mm thick high porosity layer
Fontainebleau sandstones (Paris basin)
  2 Porosities: ‘stiff’ 6% and ‘soft’ 21 %
  Mean grain size d50 ~ 260 µm
  100% quartz
[Couture 2020]
[Fonseca et al. 2013]
Notes: The materials studied: sandstones

## Slide 6
Materials
Callovo-Oxfordian clay rock (eastern France – Meuse/Haute Marne URL):
  Depth: -490 m
  Porosity ~18 %
  15-25 % quartz, 25-35 % carbonates, 40-60 % clay (illite, smectite), ~2 % pyrite
  Pre-consolidation pressure: ~10 MPa
  In situ permeability: ~10-20 m2
[Robinet et al. 2012]
SEM
X-ray CT
[Di Donna et al. 2022]
Notes: And a clay rock

## Slide 7
Experimental Devices
Major Stress 1
(max. 750 MPa)
Minor stress 3
(Max. 100MPa)
1
2
3
Intermediate stress 2 (Max. 450 MPa)
σ3
σ1
σ2
True triaxial cell with visualising device:
  Independent principal stresses loading with fixed directions
  Confining pressure 100 MPa, max. major stress 750 MPa
  Prismatic specimen size: H 50 mm, W 25 mm, T 30 mm
  Stress or displacement control in directions 1 and 2
  Window (sapphire) in direct contact with specimen surface perpendicular to direction 2
  Synthetic speckle on the visible surface
  Lubrication of the 6 specimen surfaces
  Rotating loading caps in direction 1 and 2
  High-resolution Camera 36 MPx, ~7µm/px
  DIC (Photowarp and then SPAM)
Bésuelle P., Lanatà P., 2016, A new true triaxial cell for field measurements on rock specimens and its use in the characterization of strain localization on a Vosges sandstone during a plane strain compression test, Geotechnical Testing Journal, vol. 39, n°5, pp. 879-890. ISSN 0149-6115, doi.org/ 10.1520/GTJ20150227.
Notes: The true-triaxial cell with a large viewport the protograph the surface of the specimens during loading.

## Slide 8
Experimental Devices
Axisymmetric triaxial cell for 3SR x-ray CT apparatus:
  Max. confining pressure 10 MPa
  Specimen size: 11 mm diameter, 22 mm height
  Scans with 8.5 µm voxel size
Axisymmetric micro-triaxial cell for ESRF ID19:
  Max. confining pressure 20 MPa
  Specimen size: 1 mm diameter, 2 mm height
  Scans with 0.7 µm voxel size
Force & displacement transducers
Self-compensated hydraulic piston
Double-wall cell (aluminium & PEEK)
hydraulic connexion
base fixed on the rotating plateau
Specimen with silicon coating (jacket) and alumine heads
Piezo-actuator
Notes: Two axisymetric cells for x-ray CT

## Slide 9
Outline
Introduction
Materials
  Red Vosges sandstone
  Callovo-Oxfordian clay rock
Experimental loading devices and in situ full field measurements
  True triaxial cell with 2D-imaging
  Triaxial cells for lab and synchrotron x-ray CT
Strain localisation and small scale deformation in sandstone
  Strain localisation macro-scale characterisation (2D-DIC)
  2D post mortem meso-scale analysis (SEM)
  3D in situ meso-scale analysis (lab x-ray CT)
Strain localisation and small scale deformation in a clay rock
  Strain localisation macro-scale characterisation (2D-DIC)
  2D post mortem micro-scale analysis (BIB-SEM)
  3D in situ meso-scale analysis (ESRF ID19 x-ray CT + 3D-DIC)
Conclusions

## Slide 10
Strain Localisation & small scale Deformation in Sandstone
P. Lanatà, 2015, Full-field experimental characterization of mechanical behaviour and failure in porous rock in plane strain compression: homogeneous deformation and strain localization, PhD thesis Univ. Grenoble.
Experimental campaign #1 on the isotropic Vosges sandstone: (coll. P. Lanatà)
  Plane strain compression tests (2 = 0) with different minor stress 3 values [20-50 MPa]
  Prismatic specimen size: H 50 mm, W 25 mm, T 30 mm
peak values in I2 vs. p
1- 3 [MPa]
v
1
Notes: We did a classical mechanical characterisation, however it's not the main focus of the presentation.

## Slide 11
Strain Localisation & small scale Deformation in Sandstone
P. Lanatà, 2015, Full-field experimental characterization of mechanical behaviour and failure in porous rock in plane strain compression: homogeneous deformation and strain localization, PhD thesis Univ. Grenoble.
Experimental campaign #1 on the isotropic Vosges sandstone: (coll. P. Lanatà)
  Plane strain compression tests (2 = 0) with different minor stress 3 values [20-50 MPa]
  Prismatic specimen size: H 50 mm, W 25 mm, T 30 mm
1
1- 3 [MPa]
Incremental shear strain
Notes: Example of what we measured thanks to the 2D DIC. Here, incremental shear strain fields, i.e., zone of active deformation during loading. Structured patterns appear well before the peak stress, and evolve up to the peak and then after, with a progressive reduction of the number of active localised bands.

## Slide 12
Strain Localisation & small scale Deformation in Sandstone
A
B
C
D
A
B
C
D
A
B
C
D
A
B
C
D
1- 3 [MPa]
v
1
s
v
s
v
s
v
P. Lanatà, 2015, Full-field experimental characterization of mechanical behaviour and failure in porous rock in plane strain compression: homogeneous deformation and strain localization, PhD thesis Univ. Grenoble.
A
B
C
D
A
B
C
D
dilating shear bands
compacting shear bands
compacting shear bands
1
1
1- 3 [MPa]
v
1- 3 [MPa]
v
20 MPa
40 MPa
50 MPa
Notes: Effect of the mean stress (confining pressure) on the strain localisation patterns (incremental shear and volume strain fields).

## Slide 13
Strain Localisation & small scale Deformation in Sandstone
P. Lanatà, 2015, Full-field experimental characterization of mechanical behaviour and failure in porous rock in plane strain compression: homogeneous deformation and strain localization, PhD thesis Univ. Grenoble.
Chart: 3 [MPa]
| 20 | 20 | 20 | 30 | 30 | 40 | 40 | 40 | 50
Orientations PIC | 32.5 | 33 | 37.5 | 37.5 | 39 | 40 | 36 | 37.5 | 39
Orientations Palier | 32.5 | 34 | 31 | 37.5 | 32.5 | 37.5 | 37.5 | 37.5 | 41.5
Pre-peak
Post-peak
peak values in I2 vs. p
Experimental campaign #1 on the isotropic Vosges sandstone: (coll. P. Lanatà)
  Plane strain compression tests (2 = 0) with different minor stress 3 values [20-50 MPa]
  Mean stress dependence on band orientation and volume strain inside band
  A difference between band orientation before peak and post-peak bands
Notes: Evolution of the pre-peak and post-peak band orientation with respect of the confining pressure.

## Slide 14
Strain Localisation & small scale Deformation in Sandstone
C. Couture, 2021, Mechanical characterization of porous sandstones in true triaxial conditions : diffuse and localized deformation, effect of anisotropy, PhD thesis Univ. Grenoble.
Couture C., Bésuelle P., 2022, A true triaxial experimental study on porous Vosges sandstone: from strain localization precursors to failure using full-field measurements, Int. J. Rock Mech. Mining Sci., vol. 153, pp. 105031, doi: 10.1016/j.ijrmms.2021.105031
Experimental campaign #2 on the isotropic Vosges sandstone: (coll. C. Couture)
  True triaxial tests at 2 constants mean stress [60 & 90 MPa] and 5 constant Lode angles [0-60°]
  Isotropic loading then deviatoric loading
  Prismatic specimen size: H 50 mm, W 25 mm, T 30 mm
  The Lode angle is defined here to be 0° for ASC (1 > 2 = 3) and 60° for ASE (1 = 2 > 3)
m \  | 0° | 15° | 30° | 45° | 60°
60 MPa | x | x | x | x | x
90 MPa | x | x | x | x | x
Notes: True-triaxial loading, a short recall of what is the Lode angle in the stress frame.

## Slide 15
Experimental campaign #2 on the isotropic Vosges sandstone: (coll. C. Couture)
  True triaxial tests at 2 constants mean stress [60 & 90 MPa] and 5 constant Lode angles [0-60°]
Strain Localisation & small scale Deformation in Sandstone
C. Couture, 2021, Mechanical characterization of porous sandstones in true triaxial conditions : diffuse and localized deformation, effect of anisotropy, PhD thesis Univ. Grenoble.
Notes: Mechanical characterisation. On the right, peak stress in the deviatoric plane.

## Slide 16
Experimental campaign #2 on the isotropic Vosges sandstone: (coll. C. Couture)
  True triaxial tests at 2 constants mean stress [60 & 90 MPa] and 5 constant Lode angle [0-60°]
Strain Localisation & small scale Deformation in Sandstone
(increment)
Notes: Observed strain localisation patterns (steps 1-3) for the two mean stresses and the five Lode angles

## Slide 17
Experimental campaign #2 on the isotropic Vosges sandstone: (coll. C. Couture)
  True triaxial tests at 2 constants mean stress [60 & 90 MPa] and 5 constant Lode angle [0-60°]
Strain Localisation & small scale Deformation in Sandstone
(increment)
Notes: zoom

## Slide 18
Experimental campaign #2 on the isotropic Vosges sandstone: (coll. C. Couture)
  True triaxial tests at 2 constants mean stress [60 & 90 MPa] and 5 constant Lode angle [0-60°]
Strain Localisation & small scale Deformation in Sandstone
Notes: Effect of the Lode angle on the shear band orientation (on the rigth)

## Slide 19
Experimental campaign #2 on the isotropic Vosges sandstone: (coll. C. Couture)
  True triaxial tests at 2 constants mean stress [60 & 90 MPa] and 5 constant Lode angles
Strain Localisation & small scale Deformation in Sandstone
C. Couture, 2021, Mechanical characterization of porous sandstones in true triaxial conditions : diffuse and localized deformation, effect of anisotropy, PhD thesis Univ. Grenoble.
Notes: The brittle-ductile transition, a combined effect of the mean stress AND the Lode angle.

## Slide 20
Experimental campaign #2 on the isotropic Vosges sandstone: (coll. C. Couture)
  True triaxial tests at 2 constants mean stress [60 & 90 MPa] and 5 constant Lode angles
Strain Localisation & small scale Deformation in Sandstone
C. Couture, 2021, Mechanical characterization of porous sandstones in true triaxial conditions : diffuse and localized deformation, effect of anisotropy, PhD thesis Univ. Grenoble.
Couture C., Bésuelle P., 2023, Three-invariants model and bifurcation analysis of deformation bands for a sandstone subjected to true triaxial loading paths, Acta Geotechnica, doi.org/10.1007/s11440-023-01811-w
Notes: Enveloppe of the stress peaks for various mean stresses and Lode angle.

## Slide 21
Experimental campaign #2 on the isotropic Vosges sandstone: (coll. C. Couture)
  True triaxial tests at 2 constants mean stress [60 & 90 MPa]
  Shear band dilatancy angle [Bésuelle, 2001]:
    Shearing with compaction:  < 0°
    Shearing with dilation:  > 0° and 5 constant Lode angles
Strain Localisation & small scale Deformation in Sandstone
Comparison of the shear band orientation (th vs. exp)
Comparison of the shear band dilatancy angle (th vs. exp)
C. Couture, 2021, Mechanical characterization of porous sandstones in true triaxial conditions : diffuse and localized deformation, effect of anisotropy, PhD thesis Univ. Grenoble.
Notes: What about volume strain associated to shear strain inside band. Dilating and compacting shear bands.

## Slide 22
Experimental campaign #3 on the anisotropic Vosges sandstone: (coll. C. Couture)
  True triaxial tests at constant mean stress [90 MPa]
  Several Lode angles [0 - 60 °]
  Several bedding orientations [0 – 90 °]
Strain Localisation & small scale Deformation in Sandstone
C. Couture, 2021, Mechanical characterization of porous sandstones in true triaxial conditions : diffuse and localized deformation, effect of anisotropy, PhD thesis Univ. Grenoble.
Notes: Introduction of the experimental campaign on the anisotropic sandstone.

## Slide 23
Experimental campaign #3 on the anisotropic Vosges sandstone: (coll. C. Couture)
  True triaxial tests at constant mean stress [90 MPa]
  Several Lode angles  [0 - 60 °]
  Several bedding orientations ω [0 – 90 °]
Strain Localisation & small scale Deformation in Sandstone
C. Couture, 2021, Mechanical characterization of porous sandstones in true triaxial conditions : diffuse and localized deformation, effect of anisotropy, PhD thesis Univ. Grenoble.
 = 0 °
 = 30 °
 = 60 °
Notes: For a given mean stress value, time evolution ot the shear strain fields for selected values of Lode angles and bedding orientations. How the strain localisation pattern can be influenced by the bedding.

## Slide 24
Experimental campaign #3 on the anisotropic Vosges sandstone: (coll. C. Couture)
  True triaxial tests at constant mean stress [90 MPa]
  Several Lode angles [0 - 60 °]
  Several bedding orientations [0 – 90 °]
Strain Localisation & small scale Deformation in Sandstone
C. Couture, 2021, Mechanical characterization of porous sandstones in true triaxial conditions : diffuse and localized deformation, effect of anisotropy, PhD thesis Univ. Grenoble.
Shear band orientation vs. bedding orientation and Lode angle
Notes: Attractor effect of the bedding on localisation, when bedding orientation is closed to the ‘natural’ shear band orientation.

## Slide 25
Strain Localisation & small scale Deformation in Sandstone
P. Lanatà, 2015, Full-field experimental characterization of mechanical behaviour and failure in porous rock in plane strain compression: homogeneous deformation and strain localization, PhD thesis Univ. Grenoble.
Experimental campaign #1 on the isotropic Vosges sandstone: (coll. P. Lanatà)
  Plane strain compression tests (2 = 0) with different minor stress 3 values [20-50 MPa]
  Damage characterisation by post mortem observations (SEM) for test at 50 MPa
  Thin slice close to the observed surface, SEM analysis & shear strain field overlapping
Zone in the main shear band (active in post-peak regime)
Zone in an early shear band (de-activated in post-peak regime)
Notes: Now, post mortem observation by SEM. Two selected areas in the major shear band and in a de-activated early band.

## Slide 26
Strain Localisation & small scale Deformation in Sandstone
P. Lanatà, 2015, Full-field experimental characterization of mechanical behaviour and failure in porous rock in plane strain compression: homogeneous deformation and strain localization, PhD thesis Univ. Grenoble.
Experimental campaign #1 on the isotropic Vosges sandstone: (coll. P. Lanatà)
  Plane strain compression tests (2 = 0) with different minor stress 3 values [20-50 MPa]
  Damage characterisation by post mortem observations (SEM) for test at 50 MPa
Zone in the main shear band (active in post-peak regime)
A
B
100 μm
A1
B1
A
B
100 μm
A1
B1
I2
R
I1
1,4
µm
px
0,7
0
A
100 μm
A1+B
100 μm
100 μm
B1
Notes: Cataclastic deformation in the major band.

## Slide 27
Strain Localisation & small scale Deformation in Sandstone
P. Lanatà, 2015, Full-field experimental characterization of mechanical behaviour and failure in porous rock in plane strain compression: homogeneous deformation and strain localization, PhD thesis Univ. Grenoble.
Experimental campaign #1 on the isotropic Vosges sandstone: (coll. P. Lanatà)
  Plane strain compression tests (2 = 0) with different minor stress 3 values [20-50 MPa]
  Damage characterisation by post mortem observations (SEM) for test at 50 MPa
A
100 μm
B1
A
B1
100 μm
I2
µm
px
0,14
0,07
0
A
100 μm
B1
100 μm
Zone in an early shear band (de-activated in post-peak regime)
Notes: Light damage in the de-activated early band

## Slide 28
Strain Localisation & small scale Deformation in Sandstone
J. Fonseca, P. Bésuelle, C. Viggiani, 2013, Micromechanisms of inelastic deformation in sandstones: an insight using x-ray micro-tomography, Géotechnique Letters, vol. 3 n° 2, pp 78-83.
Experimental campaign #4 on Fontainebleau sandstones: (coll. J. Fonseca & C. Viggiani)
  Axisymetric compression tests at 2 & 7 MPa confining pressures
  Damage characterisation by in operando x-ray CT (3SR)
Soft FBS03-2MPa FBS04-2MPa FBS02-7MPa
6
7
6
1
Stiff FBH01-2MPa at different loading steps
2
3
4
1
Notes: Now, 3D observations thanks to in operando x-ray CT. Two Fontainebleau sandstones, one soft (porous), the other stiff (less porous).

## Slide 29
Strain Localisation & small scale Deformation in Sandstone
J. Fonseca, P. Bésuelle, C. Viggiani, 2013, Micromechanisms of inelastic deformation in sandstones: an insight using x-ray micro-tomography, Géotechnique Letters, vol. 3 n° 2, pp 78-83.
Experimental campaign #4 on Fontainebleau sandstones: (coll. J. Fonseca & C. Viggiani)
  Damage characterisation by in operando x-ray CT --- SOFT Sandstone
6
7
6
1
Soft FBS03-2MPa FBS04-2MPa FBS02-7MPa
  Strain localisation observed visually after peak stress
  No damage observed before peak, given the x-ray CT scan resolution (8.5 µm) – however could possibly start before
  Intra-granular cracking at peak, small fragments, grain rearrangement.
  Cracking initiates at grain contact, depending on the contact surface, with sub-vertical alignement, influenced by the grain coordination
Notes: Grains cracking for the soft sandstone. Effect the grain-to-grain contact shape.

## Slide 30
Strain Localisation & small scale Deformation in Sandstone
J. Fonseca, P. Bésuelle, C. Viggiani, 2013, Micromechanisms of inelastic deformation in sandstones: an insight using x-ray micro-tomography, Géotechnique Letters, vol. 3 n° 2, pp 78-83.
Experimental campaign #4 on Fontainebleau sandstones: (coll. J. Fonseca & C. Viggiani)
  Damage characterisation by in operando x-ray CT --- STIFF Sandstone
Stiff FBH01-2MPa at different loading steps
2
3
4
1
  Strain localisation observed before peak stress
  Damaging of the cement between grains, along vertical ridges, formation of vertical columns of horizontaly undounded grains
  Intra-granular cracking inhibited dut to extended grain contacts
  As shearing progresses, vertical columns eventually collapse, unbounded grains increases shear band thickness
Notes: Grain debonding in the stiff sandstone to form sub-axial columns.

## Slide 31
Outline
Introduction
Materials
  Red Vosges sandstone
  Callovo-Oxfordian clay rock
Experimental loading devices and in situ full field measurements
  True triaxial cell with 2D-imaging
  Triaxial cells for lab and synchrotron x-ray CT
Strain localisation and small scale deformation in sandstone
  Strain localisation macro-scale characterisation (2D-DIC)
  2D post mortem meso-scale analysis (SEM)
  3D in situ meso-scale analysis (lab x-ray CT)
Strain localisation and small scale deformation in a clay rock
  Strain localisation macro-scale characterisation (2D-DIC)
  2D post mortem micro-scale analysis (BIB-SEM)
  3D in situ meso-scale analysis (ESRF ID19 x-ray CT + 3D-DIC)
Conclusions

## Slide 32
Strain Localisation & small scale Deformation in a Clay Rock
Experimental campaign #1 on the Callovo-Oxfordian clay rock:
  Plane strain compression tests (2 = 0) with different minor stress 3 values [2-20 MPa]
  Horizontal bedding
  Prismatic specimen size: H 50 mm, W 25 mm, T 30 mm
peak values in I2 vs. p
1- 3 [MPa]
v
1
deviatoric plane
Notes: The same with a clay rock

## Slide 33
Strain Localisation & small scale Deformation in a Clay Rock
Experimental campaign #1 on the Callovo-Oxfordian clay rock:
  Plane strain compression tests (2 = 0) with different minor stress 3 values [2-20 MPa]
3 = 2 MPa
3 = 12 MPa
Notes: Two examples of the time evolution of the incremental shear strain fields for a low and higher confining pressures.

## Slide 34
Strain Localisation & small scale Deformation in a Clay Rock
Experimental campaign #1 on the Callovo-Oxfordian clay rock:
  Plane strain compression tests (2 = 0) with different minor stress 3 values [2-20 MPa]
3 = 2 MPa
3 = 12 MPa
normal gap
tangential gap
Notes: Normal and tangential components the displacement jump.

## Slide 35
Strain Localisation & small scale Deformation in a Clay Rock
Experimental campaign #2 on the Callovo-Oxfordian clay rock:
  Plane strain compression tests (2 = 0) with two minor stress 3 values [2 & 12 MPa]
  Assessment of anisotropy: effect of bedding orientation
peak stress vs. bedding orientation
1- 3 [MPa]
v
1
3 = 2 MPa
3 = 12 MPa
Notes: Anisotropy in the clay rock on mechanical response

## Slide 36
Strain Localisation & small scale Deformation in a Clay Rock
Experimental campaign #2 on the Callovo-Oxfordian clay rock:
  Plane strain compression tests (2 = 0) with two minor stress 3 values [2 & 12 MPa]
  Assessment of anisotropy: effect of bedding orientation
3 = 2 MPa
3 = 12 MPa
15°
80°
24°
53°
12°
0°
45°
77°
50°
Fault orientation [°]
Fault orientation [°]
Bedding orientation [°]
Bedding orientation [°]
Fault // bedding
Fault // bedding
Notes: Examples of possible interactions between bedding and shear localisation.

## Slide 37
Strain Localisation & small scale Deformation in a Clay Rock
Experimental campaign #1 on the Callovo-Oxfordian clay rock: (coll. G. Dubois, J. Urai et al.)
  Plane strain compression tests (2 = 0) with different minor stress 3 values [2-20 MPa]
  Microstructure observation by BIB-SEM
Desbois G., Höhne N., Urai J.L., Bésuelle P., Viggiani G., 2017, Deformation in cemented mudrock (Callovo-Oxfordian Clay) by microcracking, granular flow and phyllosilicate plasticity: insights from triaxial deformation, broad ion beam polishing and scanning electron microscopy, Solid Earth, vol. 8, pp. 291-305. .
Notes: Hight resolution observations by BIB-SEM of the microstructure after unloading in four selected areas.

## Slide 38
Strain Localisation & small scale Deformation in a Clay Rock
Experimental campaign #1 on the Callovo-Oxfordian clay rock: (coll. G. Dubois, J. Urai et al.)
  Plane strain compression tests (2 = 0) with different minor stress 3 values [2-20 MPa]
  Microstructure observation by BIB-SEM
Desbois G., Höhne N., Urai J.L., Bésuelle P., Viggiani G., 2017, Deformation in cemented mudrock (Callovo-Oxfordian Clay) by microcracking, granular flow and phyllosilicate plasticity: insights from triaxial deformation, broad ion beam polishing and scanning electron microscopy, Solid Earth, vol. 8, pp. 291-305. .
ROI-2
Notes: In the cluster of conjugated bands

## Slide 39
Strain Localisation & small scale Deformation in a Clay Rock
Experimental campaign #1 on the Callovo-Oxfordian clay rock: (coll. G. Dubois, J. Urai et al.)
  Plane strain compression tests (2 = 0) with different minor stress 3 values [2-20 MPa]
  Microstructure observation by BIB-SEM
Desbois G., Höhne N., Urai J.L., Bésuelle P., Viggiani G., 2017, Deformation in cemented mudrock (Callovo-Oxfordian Clay) by microcracking, granular flow and phyllosilicate plasticity: insights from triaxial deformation, broad ion beam polishing and scanning electron microscopy, Solid Earth, vol. 8, pp. 291-305. .
Notes: With the legend

## Slide 40
Strain Localisation & small scale Deformation in a Clay Rock
Experimental campaign #1 on the Callovo-Oxfordian clay rock: (coll. G. Dubois, J. Urai et al.)
  Plane strain compression tests (2 = 0) with different minor stress 3 values [2-20 MPa]
  Microstructure observation by BIB-SEM
Desbois G., Höhne N., Urai J.L., Bésuelle P., Viggiani G., 2017, Deformation in cemented mudrock (Callovo-Oxfordian Clay) by microcracking, granular flow and phyllosilicate plasticity: insights from triaxial deformation, broad ion beam polishing and scanning electron microscopy, Solid Earth, vol. 8, pp. 291-305. .
Notes: In the major fault

## Slide 41
Strain Localisation & small scale Deformation in a Clay Rock
Experimental campaign #1 on the Callovo-Oxfordian clay rock: (coll. G. Dubois, J. Urai et al.)
  Plane strain compression tests (2 = 0) with different minor stress 3 values [2-20 MPa]
  Microstructure observation by BIB-SEM
Desbois G., Höhne N., Urai J.L., Bésuelle P., Viggiani G., 2017, Deformation in cemented mudrock (Callovo-Oxfordian Clay) by microcracking, granular flow and phyllosilicate plasticity: insights from triaxial deformation, broad ion beam polishing and scanning electron microscopy, Solid Earth, vol. 8, pp. 291-305. .
Notes: Deduced scenario of mechanisms of deformation during loading

## Slide 42
Strain Localisation & small scale Deformation in a Clay Rock
Experimental campaign #3 on the Callovo-Oxfordian clay rock: (coll. E. Ando et al.)
  Axisymetric compression tests with minor stress 3 value [5 & 20 MPa]
  Specimen size: 1 mm diameter, 2 mm height
  in operando X-ray CT at ID19 (ESRF): voxel size 0.7 µm
1- 3 [MPa]
100µm
1
10µm
Notes: Now, high resolution 3D in operando images during triaxial loading on a very small sample. A complex microstructure with different mineral inclusions imbedded in a textured clay matrix.

## Slide 43
Strain Localisation & small scale Deformation in a Clay Rock
Experimental campaign #3 on the Callovo-Oxfordian clay rock: (coll. E. Ando et al.)
  Axisymetric compression tests with minor stress 3 value [5 & 20 MPa]
  Specimen size: 1 mm diameter, 2 mm height
  in operando X-ray CT at ID19 (ESRF): voxel size 0.7 µm
Notes: Time evolution of the meso-structure: faulting

## Slide 44
Strain Localisation & small scale Deformation in a Clay Rock
Experimental campaign #3 on the Callovo-Oxfordian clay rock: (coll. E. Ando et al.)
  Axisymetric compression tests with minor stress 3 value [5 & 20 MPa]
  Specimen size: 1 mm diameter, 2 mm height
  in operando X-ray CT at ID19 (ESRF): voxel size 0.7 µm
Notes: Zoom: grain debonding and faulting

## Slide 45
Strain Localisation & small scale Deformation in a Clay Rock
Experimental campaign #3 on the Callovo-Oxfordian clay rock: (coll. E. Ando et al.)
  Axisymetric compression tests with minor stress 3 value [5 & 20 MPa]
  Specimen size: 1 mm diameter, 2 mm height
  in operando X-ray CT at ID19 (ESRF): voxel size 0.7 µm
  DIC (Spam) analysis - ongoing work with E. Ando and O. Stamati
    Continuous DIC: many ‘homogenous’ (without texture) mineral inclusions !
    Discrete DIC: ok for mineral inclusions (if powerfull grain segmentation…), not for clay matrix !
    Mixing continuous + discrete: ok for both clay matrix and mineral inclusions
    Ongoing task: improving grain segmentation
      Based on both grey level + variance: ok but…
      Deep learning ?
    Objectives: quantify micro-mechanisms of deformation at mesoscale (grain debonding, grain breakage, etc…)
X-ray CT + discrete V-DIC on a sand [Ando, 2015]
Notes: V-DIC measurement (in progress work)

## Slide 46
Strain Localisation & small scale Deformation in a Clay Rock
Experimental campaign #3 on the Callovo-Oxfordian clay rock: (coll. E. Ando et al.)
  Axisymetric compression tests with minor stress 3 value [5 & 20 MPa]
  Specimen size: 1 mm diameter, 2 mm height
  in operando X-ray CT at ID19 (ESRF): voxel size 0.7 µm
Notes: Time evolution of the incremental shear strain field

## Slide 47
Strain Localisation & small scale Deformation in a Clay Rock
Self-sealing experiment on the Callovo-Oxfordian clay rock: (coll. A. Di Donna et al.)
  Self-sealing experiment with synthetic crack
  Specimen size: 12 mm diameter, 20 mm height
  Oedometric conditions
  in operando X-ray CT at 3SR Lab & ID19 (ESRF): voxel size 0.7 µm
Di Donna A., Charrier P., Dijkstra J., Andò E., Bésuelle P., 2022, The contribution of swelling to self-sealing of claystone studied through x-ray tomography, Phys. Chem. Earth, Part A, vol. 127, pp. 103191, doi : 10.1016/j.pce.2022.103191.
Notes: Not presented – sealf sealing tests in the clay rock.

## Slide 48
Strain Localisation & small scale Deformation in a Clay Rock
3SR x-ray CT
voxel size 7.5 µm
10’
ID19 x-ray CT
voxel size 0.7 µm
5’
Self-sealing experiment on the Callovo-Oxfordian clay rock: (coll. A. Di Donna et al.)
  Self-sealing experiment with synthetic crack
  Specimen size: 12 mm diameter, 20 mm height
  Oedometric conditions
  in operando X-ray CT at 3SR Lab & ID19 (ESRF): voxel size 0.7 µm
Di Donna A., Charrier P., Dijkstra J., Andò E., Bésuelle P., 2022, The contribution of swelling to self-sealing of claystone studied through x-ray tomography, Phys. Chem. Earth, Part A, vol. 127, pp. 103191, doi : 10.1016/j.pce.2022.103191.
Notes: Not presented – sealf sealing tests.
Hight resolution x-ray CT scans to observed a short-term sealing process by micro-faulting to fill the initial (synthetic) fault (before a long term swelling – not shown here)

## Slide 49
Conclusions
3D full field measurement well adapted for axisymetric loading condition
True-triaxial loading accessible for 2D DIC
2D DIC fields used to define investigation zones by microscopy
  one can go back to the loading history if we identify zones that have been deactivated during loading
  However, post mortem analysis problematic
3D imaging: need to adapt the spatial resolution to the material microstructure:
  small specimen for fine microstructure, limits are evolving, however, technical difficulties
Notes: The end.